System Verilog Project AHB Lite Protocol

Transaction
Can I run predefined sequences? (e.g. reset sequence, random write sequence, random read/write bursts, a directed test). Can I debug easily if my test fails? Do I need one or multiple transactions for bursts?
Answer:
Yes,we can run the predefined sequence (e.g. reset sequence, random write sequence, random read/write bursts, a directed test).Yes we had make the print_trans function in the transaction class to see the values of all inputs and outputs and it help in debugging where the test fails. We need four transaction for the increment4 and wrap4 burst transfer and for single transfer we need only one transaction.

Generator
How to control how many transactions get generated? Sometimes random transactions are not needed. How do I generate non-random transactions when required?
Answer:
In generator we declare a variable repeat_Count and the run the loop to repeat_count times to generate the as many transactions as the value of repeat_count. If value of repeat count is 10 then 10 number of transactions are generated. Yes we can generate the nonrandom values by turning off the random mode of all transaction elements and write the pre_randomize function to initiate the values of transaction elements.

Driver
Are the interface signals driven according to the spec? Does the transaction have proper address/data Phases? Do I need to sample inputs to decide whether to drive outputs or not on the next clocking event?
Answer:
Yes, the interface signals driven according to the spec,Yes the transaction have proper address/data Phases .The data is sample at the posedge of the clock.

Monitor
Are the interface signals sampled according to the spec? Does the transaction have proper address/data Phases?
Answer:
Yes, the interface signals driven according to the spec,Yes the transaction have proper address/data Phases.

Scoreboard
Does the scoreboard implement proper endianness? How to change endianness if required? How to not compare reset values and to compare only those memory locations which have already been written?
Should scoreboard memory be static or dynamic?
Answer:
I know that I have to set the bit endianness 0 for the little endian and 1 for the big endian respectively. We can check the memory location which is already written by the address.
Scoreboard memory is static because memory allocation is done at the the compilation time.